## Slide 1
Training Publication SPI-06
Rev 1
24 Dec 2025
by Konrad Burgoyne MIMF, FSPI
Understanding Process Failure Mode and Effects Analysis (PFMEA)

## Slide 2
Information
This training publication is provided for educational purposes and may be freely shared, copied and distributed. It is not subject to copyright restrictions.

## Slide 3
Introduction
AIM: To establish a common understanding for effective process risk identification, assessment, mitigation and prevention.

## Slide 4
PFMEA is usually conducted as part of New Product Introduction (NPI)
PFMEA can equally be applied to products currently in production when the manufacturing processes are changed or being addressed for improvement
Process Failure Mode and Effects Analysis
A failure mode is a cause of failure or a potential way a system can fail

## Slide 5
PFMEA is a risk identification and assessment for processes usually directly associated with manufacturing.
Process Failure Mode and Effects Analysis
A process change is a change in material, method and/or measurement technique that can potentially affect form, fit or function

## Slide 6
So, what is it?
A PFMEA provides a structured, qualitative, analytical framework which taps the multi-disciplined experience of the team to brainstorm answers to such questions as:
How can this process, function, facility, or tooling fail?
What effect will failure have on the end product (or customer)?
How can potential failures be eliminated or controlled?
Process Failure Mode and Effects Analysis

## Slide 7
PFMEA is accomplished using a cross-functional team that may include, manufacturing engineers, subject matter experts, process operators, quality engineers and process planners.
Process Failure Mode and Effects Analysis
Effects analysis is a method of understanding and addressing the potential effects of failure

## Slide 8
Process Failure Mode and Effects Analysis
Process Flow Diagram
Process Failure Mode and Effects Analysis
Control Plan
Product Key Characteristics
Measurement Systems Analysis
Work Instructions
Product and Processes Key Characteristics
Design Risk Analysis
AS13004 Scope
Scope of this training
Information Relationships

## Slide 9
Inputs to developing a PFMEA should include the following: -
Process Flow Diagram
Identification of all steps within each operation
Non-conformance data for similar products and processes, including lessons learned
Characteristics Matrix
Design Risk Analysis (e.g., DFMEA)
Existing PFMEA on similar products and processes
Product KCs (including customer defined KCs)
Process KCs (potential or as defined in the design records)
Control Plan from similar processes
Process Failure Mode and Effects Analysis

## Slide 10
Process Flow Diagram (PFD)
A Process Flow Diagram (PFD) shows the relations between major components in a system

## Slide 11
Process Flow Diagram (PFD)
Operation
100 – CNC Drill set-up
Description
People
Inputs
Outputs
Documents
Process KC
Product KC
Controls
Select correct NC program
Process Operator
Barcode on job card
Job card
Barcode on job card
Laser tool checker automated verify
200 – Tool set-up
Select correct tooling
Process Operator
Barcode on job card
Job card
NC program
Tooling
Material kitted by computer system
300 – Load material
Select correct material
Process Operator & Stores
Material. BoM kitting
Job card & BoM
Material specification
400 – Run CNC production
Machine to drawing
Process Operator
Machined part
500 – Inspection verification
Inspect to drawing
Inspector
Conforming part
Inspection sign off on job card
Operator sign off on job card
Completed operation
Conforms to drawing
Drawing
Job card sign off
Job card sign off

## Slide 12
Process Flow Diagram Example – Flow Symbols

## Slide 13
Process Failure Mode and Effects Analysis
Process Definition
Process Flow Diagram (PFD)
Process Characteristics
Documented Assessment
PFMEA
Control Strategy
Control Plan
Error Proofing
Customer Requirements
Design Data & Drawing
Standards & Specifications
Purchase Order & Contract Review
Manufacturing
Work Instructions
Process Control Documents
Job Card
Product Definition
Key Characteristics & Critical Items
Special Requirements
DFMEA
AS13004 Scope
Scope of this training
Information Flow

## Slide 14
Outputs from the development of a PFD should include:
Details of all operations in sequential order from receipt of materials through storage and shipment of finished product. This encompasses alternative processes, standard rework and movement of product from operation to operation as well as to and from external operations.
Process Failure Mode and Effects Analysis
A Process Flow Diagram (PFD) shows the relations between major components in a system.

## Slide 15
Process Failure Mode and Effects Analysis
6 Steps of PFMEA

## Slide 16
STEP 1: Review the process
Use a process flow diagram to identify each process component.
List each process component in the FMEA table.
If it starts feeling like the scope is too big, it probably is. This is a good time to break the Process Failure Mode and Effects Analysis into more manageable chunks

## Slide 17
STEP 2: Brainstorm potential failure modes
Review existing documentation and data for clues about all of the ways each component can failure.
The list should be exhaustive – it can be paired down and items can be combined after this initial list is generated.
There will likely be several potential failures for each component

## Slide 18
STEP 3: List potential effects of each failure
The effect is the impact the failure has on the end product or on subsequent steps in the process.
There will likely be more than one effect for each failure.

## Slide 19
STEP 4: Calculate the Risk Priority Number(RPN)
Based on the severity of the consequences of failure.
Rate the severity of each effect using customized ranking scales as a guide. What are the chances the failure will be detected prior to it occurring.
Severity X Occurrence X Detection

## Slide 20
STEP 5: Develop & Implement the action plan
Decide which failures will be worked on based on the Risk Priority Numbers. Focus on the highest RPNs.
Define who will do what by when. Implement the improvements identified by your Process Failure Mode and Effects Analysis team.

## Slide 21
STEP 6: Calculate the resulting RPN
Re-evaluate each of the potential failures once improvements have been made and determine the impact of the improvements.

## Slide 22
Example Documentation
Example Forms
Downloadable Microsoft Excel file can be found here:
https://sp-i.org/downloads.html

## Slide 23
Example PFD 1 Form
Export Control Classification |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Other restrictions |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PROCESS FLOW DIAGRAM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PART NUMBER/S: |  |  |  |  |  |  |  |  |  |  |  |  | PREPARED BY: |  |  | 
PART / FAMILY DESCRIPTION: |  |  |  |  |  |  |  |  |  |  |  |  | DATE: |  |  | 
OPERATION | STEP | ADMINISTRATION | PACKAGING INTERACTION | LIFT (mechanical / other) | LOAD / INSTALL | FABRICATION / TRANSFORMATION STEP | MOVE | STORE | INSPECT | REWORK | OTHER (SPECIFY) | OPERATION DESCRIPTION | CLASSIFICATION | PRODUCT KC | PROCESS KC | CONTROL METHODS

## Slide 24
Example PFD 2 Form
Export Control Classification |  |  |  |  |  |  |  | 
Other restrictions |  |  |  |  |  |  |  | 
PROCESS FLOW DIAGRAM |  |  |  |  |  |  |  | 
Process |  |  |  |  |  |  |  | 
Prototype - Pre-Launch - Production - |  |  |  |  |  |  | Date (Orig.) | 
Key Contact |  | Core Team |  |  |  |  | Date (Rev.) | 
 |  |  |  |  |  |  | Customer Approval Date | 
PROCESS DESCRIPTION | OPERATION | STEP | INPUTS | CLASSIFICATION | OUTPUTS | CONTROLS | MISTAKE PROOFING | REMARKS
 |  |  |  |  |  |  | Rev - | 

## Slide 25
Example PFMEA Form
Export Control Classification |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Other restrictions |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Process Failure Mode and Effects Analysis (PFMEA) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototype - Pre-Launch- Production - |  |  |  |  | Key Contact / Phone |  |  |  |  |  | Date (Orig.) |  |  | Date (Rev.) |  |  |  |  |  | 
Part Number |  |  |  |  | Core Team |  |  |  |  |  | Customer Approval Date |  |  |  |  |  |  |  |  | 
Operation | Step | Process Function/ Description | Requirements | Potential Failure Mode | Potential Effect(s) of Failure | Severity | Classification | Potential Cause(s) of Failure | Current Process |  |  |  | RPN | Recommended Action | Responsibility & Target Completion Date | Action Results |  |  |  | 
 |  |  |  |  |  |  |  |  | Prevention Controls | Occurrence | Detection Controls | Detection |  |  |  | Actions Taken Completion Date | Severity | Occurrence | Detection | RPN
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Rev - |  |  |  | 

## Slide 26
Example Control Plan Form
Export Control Classification |  |  |  |  |  |  |  |  |  |  |  |  | 
Other restrictions |  |  |  |  |  |  |  |  |  |  |  |  | 
Control Plan |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototype - Pre-Launch- Production - |  |  |  |  | Key Contact / Phone |  |  |  | Date (Orig.) |  | Date (Rev.) |  | 
Part Number |  |  |  |  | Core Team |  |  |  | Customer Approval Date |  |  |  | 
Part Name / Description |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | Step | Process Function / Description | Machine, Device, Jig, Tools For Mfg. | Characteristics |  |  | Classification | Methods |  |  |  |  | Reaction Plan
 |  |  |  | # | Product | Process |  | Requirements | Evaluation / Measurement Technique | Sample |  | Control Method | 
 |  |  |  |  |  |  |  |  |  | Size | Freq |  | 

## Slide 27
Questions?

## Slide 28
Revision Control
sp-i.org
email@sp-i.org
Rev | Date | Change | Author
1 | 24 Dec 2025 | Established training slide pack with the guidebook | Konrad Burgoyne